## Slide 1
SHRI SHIVAJI SCIENCE COLLEGE, AMRAVATI
( Department Of Computer Soft.)
“Edge AI for real time image and video analysis in IOT device”
Submitted BY
Ms. Nisha S. Mokashe
Guided By
Dr. B. R. Jalamkar

## Slide 2
Introduction
Objective
Need for Edge Computing
WebRTC and RTSP Overview
Proposed Architecture
Google Coral and Intel Compute Stick 2
Methodology
Experimental Results
Conclusion and Future Work
References
CONTENTS =>

## Slide 3
INTRODUCTION
IoT devices have grown significantly,from 13% in 2014
to 25% today, with 43 billion connected devices in 2023.
Real-time data processing is crucial, especially in remote
surveillance systems using edge devices.
Cloud computing struggles with transmission power,
bandwidth, and latency issues, necessitating edge-based
solutions.

## Slide 4
Objective
Propose an architecture that allows small businesses to process real-time video on IoT devices using edge AI technologies.
The architecture is:
- Easy to implement
- Cost-effective
- Processes video in real-time
- Enhances flexibility and security using
accelerators such as Google Coral and Intel Neural Compute Stick 2.

## Slide 5
Need for Edge Computing :
Cloud-based video surveillance systems require high data transfer rates (2.3 Mbps for a single H.265 1080p camera at 15 FPS).
Cloud systems introduce latency of hundreds of milliseconds, which is critical for safety applications (e.g., pedestrian detection).
Privacy risks exist with cloud-based video transmission, leading to privacy and legal challenges (e.g., GDPR compliance).

## Slide 6
WebRTC and RTSP Overview :
WebRTC: Enables real-time peer-to-peer video streaming with low latency,
written in JavaScript and supported by most browsers.
• RTSP: Protocol for real-time streaming of media, commonly used in IP
cameras and IoT devices.
• Both are key protocols for real-time video analysis in IoT systems.

## Slide 7
Proposed Architecture :
Interior Transfer Component: Captures and processes video frames using
AI accelerators (Google Coral, Intel NCS2).
• Exterior Transfer Component: Manages transfer of processed data to
browsers via WebRTC.
• Process Data Component: Handles user requests like object detection,
recognition, and blurring.

## Slide 8
Google Coral and Intel Compute Stick 2 :
Google Coral: Edge TPU for AI tasks, supporting TensorFlow Lite models, achieving 400 FPS for image classification.
• Intel Compute Stick 2: Powered by Intel Movidius VPU, optimized for
real-time image analysis using OpenVINO toolkit.

## Slide 9
Methodology :
Data Preparation: Collect and curate datasets.
• Data Augmentation: Apply transformations like flipping and brightness
adjustments.
• Transfer Learning: Fine-tuning the MobileNetV2 architecture for object
detection
• Training and Fine-tuning: Use pre-trained models and refine for IoT
device deployment.

## Slide 10
Experimental Results :
Google Coral: Achieved 55 FPS in indoor tests, stable real-time processing.
• Intel NCS2: Under 1 second latency in cross-country tests
(Japan to Vietnam).
• Both accelerators meet real-time performance requirements.

## Slide 11
Conclusion and Future Work :
Conclusion: Architecture is efficient for real-time IoT video and image analysis, achieving low latency and high performance.
• Future Work: Improve resolution, cross-platform compatibility, and
performance with additional accelerators.

## Slide 12
References :
J. Fredrik Dahlqvist, M. Patel, A. Rajko, "Growing opportunities in the Internet of Things," McKinsey & Company, 2019.
2. S. Loreto, S. Romano, "Real-Time Communication with WebRTC: Peer-to-Peer in the Browser," O'Reilly Media, 2014.
3. Google Coral Documentation, [Accessed 2023].

## Slide 13
THANK YOU